OpenFastPath performance measurement procedure.

OpenFastPath (OFP) is a high performance data-plane stack designed to scale linearly on multi-core and to have the best performance per core.
OFP utilizes the functionality provide by OpenDataPlane (ODP) to achieve maximum input / output packet performance. As the ODP implementation is dependent on the used network interface controller (NIC), the available hardware acceleration may differ.
# Configuration details
Application configuration details:
ODP Version
OFP commit number
OFP configure parameters
OFP code changes (attach patch file)

Hardware and software platform configuration details:
HW Version
SDK Version
Core Frequency / IO Frequency
NIC Interfaces

# Use-case: IP Forwarding
The following test describes a pure IP forwarding use-case. Using the information in the route and arp tables, received packets are sent to the appropriate interface based on the packets IP header.
### Test set up description
IP traffic is sent from a packet generator (node 1) to a destination (node 3) by using a forwarding node 2 with OFP application running and configured for this operation.
OFP application on node 2 forwards IP traffic from interface fp0 to interface fp1 using the route table and ARP table entries.

2
1
3

192.168.10.1	192.168.20.2	192.168.20.1

### Procedure
Start application that uses OFP on node 2. Ex:
./fpm -i interface0,interface1 -c 3 -p
Connect with telnet to OFP CLI on port 2345. To connect remotely you need to have a management interface/IP on node 2.
telnet 127.0.0.1 2345
Configure IPs on fpX interfaces with commands:
ifconfig fp0 192.168.10.2/24
ifconfig fp1 192.168.20.2/24
1. Ping node 2 from node 3 in order to populate the ARP table. Doing this prior to the high load test start avoids the loss of ARP responses due to depleted packet buffers. I.e. before they can be handled by the normal ARP request / ARP response procedure.
2. Generate traffic from packet generator (node 1)
3. Collect results from destination (node 3) or from OFP application (node 2).
NOTE 1: Target configuration
OFP target configuration snapshot from CLI:
> route
Destination Gateway Iface
192.168.10.2/24 0.0.0.0 fp0
192.168.20.2/24 0.0.0.0 fp1
> arp
VRF ADDRESS MAC AGE
0 192.168.10.1 ec:9e:cd:0e:36:a2 27
0 192.168.20.1 ec:9e:cd:0e:36:a3 27
NOTE 2: target machines
Node 1 and node 3 can be a single machine or Spirent/Ixia traffic generator with two real interfaces and IP addresses assigned in two networks and connected to node 2.

### Results
IPv4 Forwarding with 64-byte frame	Performance in Mpps
1 core (“-c 3” parameter)
2 core (“-c 5” parameter)
4 core (“-c 7” parameter)

# Use-case: UDP Forwarding
The following test describes a UDP forwarding use-case.
### Test set up description
UDP packets are sent from a packet generator (node 1) to multiple destination sockets on node 2, these are then forwarded to a single socket on node 3.
Udp_fwd_sock OFP application is used to forward UDP packets received on interface fp0 to node 3 through interface fp1.
fp0	fp1
2
1
3

        192.168.10.2:5001[,5002[,…]]]	192.168.20.1:5000

### Procedure
Start OFP application on node 2:
./udp_fwd_sock -i interface0,interface1 -c 3 -l 192.168.10.2 -r 192.168.20.1 -s 1
Connect with telnet to OFP CLI on port 2345. To connect remotely you need to have a management interface/IP on node 2.
telnet 127.0.0.1 2345
Configure IPs on fpX interfaces with commands:
> ifconfig fp0 192.168.10.2/24
> ifconfig fp1 192.168.20.2/24
1. Ping node 2 from node 3 in order to populate the ARP table. Doing this prior to the high load test start avoids the loss of ARP responses due to depleted packet buffers. I.e. before they can be handled by the normal ARP request / ARP response procedure.
2. Generate traffic from packet generator (node 1)
3. Collect results from destination (node 2).
NOTE 1: Target configuration
OFP target configuration snapshot from CLI:
> route
Destination Gateway Iface
192.168.10.2/24 0.0.0.0 fp0
192.168.20.2/24 0.0.0.0 fp1
> arp
VRF ADDRESS MAC AGE
0 192.168.10.1 ec:9e:cd:0e:36:a2 27
0 192.168.20.1 ec:9e:cd:0e:36:a3 27
NOTE 2: Target machines
Node 1 and node 3 can be a single machine or Spirent/Ixia traffic generator with two real interfaces and IP addresses assigned in two networks and connected to node 2.

### Results
UDP Forwarding, 64B frame, one source socket on node 1 per destination socket	Mpps with one socket	Mpps with 2 sockets	Mpps with 4 sockets
1 core (“-c 3” parameter)
2 core (“-c 5” parameter)
4 core (“-c 7” parameter)

UDP Forwarding, 64B frame, 100K sources sockets on node 1
1 core (“-c 3” parameter)
2 core (“-c 5” parameter)
4 core (“-c 7” parameter)